Course on Internet of Things
# Exercises Session 3: Switches
## Introduction:
Switches exist in various incarnations. There are the simple mechanical switches: on/off or push button switches but there are also switches than turn on or off with various external conditions:
- temperature
- infra red radiation (e.g. the Passive Infrared Sensor or PIR sensor)
- Hall switches detecting magnetic field
- microphone switches which turn on when a certain noise level is detected
In this exercise we will use a mechanical push button switch and a PIR sensor
Mechanical Switch	PIR sensor

## Exercise 1:
The push button switch is connected to GPIO 17 on the ESP32 board.
Write a script that polls the state of the switch every 100 ms and prints state changes (only print out a message when the switch state has changed). Catch <ctrl> C to smoothly exit the program.
Check https://docs.micropython.org/en/latest/esp8266/tutorial/pins.html and https://docs.micropython.org/en/latest/esp32/quickref.html for information on how to accomplish this.
## Exercise 2:
Do the same thing as in exercise 1 but use external interrupts and a callback routine to do the job.
## Exercise 3:
Combine this exercise with the exercise on LEDs: Switch the builtin LED on when the button is pressed and off when it is released
## Exercise 4:
Write a program scanning the PIR sensor, indicating if a person is close. The PIR sensor, just like the push button, uses a single GPIO line as input. The boards allows to choose which GPIO to use and I selected D4 = GPIO 16
## Exercise 5:
The sensor kit in the lab contains a big number of sensors acting like switches:
- rolling ball switch
- mercury switch
- noise level detector (microphone)
- hall sensor (detecting magnetic field)
- reed relay (detecting magnetic field)
- and many more...
Connect these sensors to the ESP32 and try them with the programs developed in exercise 1-3